| SPECIFICATION FOR APPROVAL |
| --- |
|  | CUSTOMER： |  | DATE： DD/MM/YYYY | 16-02-2008 |  |
|  | CUSTOMER P/N： |  |  |  |
|  | C.T.C. P/N： | CH6080330K-542319-T | SAMPLEQ’TY： |  |  |
|  | PRODUCT NAME： | CH6080UTB-330K-035-VER00 |  |
|  | DRAWN BY: | CHECKED BY: | APPROVED BY: |  |
|  | Yu Xinze | Jiang Tianming | Tao Guowen |  |
|  | APPROVED BY CUSTOMER |  |
|  |  | SIGNATURE | DATE |  |
|  | APPROVED |  |  |  |
|  | CONDITIONAL APPROVED |  |  |  |
|  | REJECTED |  |  |  |
|  | C.T.C. Coils Limited 確力新實業有限公司 香港新界大埔汀角路55號太平工業中心2座8字樓E室 Flat E, 8/F, Block 2, Tai Ping Ind. Centre, 55 Ting Kok Rd., Tai Po., N.T., Hong Kong Tel : (852) 2695-4889 Fax : (852) 2695-1842 http://www.ctccoils.com E-mail : enquiry@ctccoils.com C.T.C. Electronics (Fonggang) Factory東莞確力新電子廠 中國廣東省東莞市鳳崗鎮雁田區南山工業城第一棟 Nanshan Industrial District, Yantian Village, Fenggang Town, Dongguan City, Guangdong Province, China, P.R.C. Tel : (86)769-7771591 Fax : (86)769-7771314 C.T.C. Electronics (Tangxia) Limited東莞確一新電子有限公司 中國廣東省東莞市塘厦林村新太陽工業城第十七棟 No.17, New Sun Industrial City, Tang Xia Town, Lin Cun, Dongguan City, Guangdong Province, China, P.R.C. Tel : (86)769-7811682 Fax : (86)769-7811382 |  |

| SPECIFICATION FOR: |  | ( ) | REF.: |  |
| --- | --- | --- | --- | --- |
| C.T.C. P/N: | CH6080330K-542319-T | DATE: DD/MM/YYYY | 16-02-2008 |  |
| PRODUCT NAME: | CH6080UTB-330K-035-VER00 |  |
| 1.DIMENSION (UNIT : mm): |
| A: | 11.0 Max. | B: | 18.0 ± 0.5 | C: | 11.0 Max. | D: | 9.0 ± 0.5 | E: | 0.65 ± 0.05 |
| F: | 5.0+0.8/-0.5 | G: | 12.5 Min. | H: | 18.0 +1.0/-0.5 | I: |  | J: |  |
| 2.ELECTRIC CHARACTERISTICS: (TEST AT：24℃ ± 4℃) |
| INDUCTANCE: | 33 uH ± 10% | TEST FREQ: | @1.0KHz/0.25V | DCR: | 0.11 Ω Max. |
| TURNS: | 33.5 TS (Ref) | IDC: | ----- A | RDC: | 1.4 A |
| Q: | 25 Min. @ 2.52 MHz | SRF: | 7.0 MHz Min. | TEMP: | -20℃ ~ +80℃ |
| 3.TEST EQUIPMENT: |
| ( | HP-4284A (LCZ-METER) | ( | CH-1062 (LCZ-METER) | ( | CH-1320(CURRENT METER) |
| ( | HP-8712C (ANALYZER) | ( | SK-3005 (INSULATION TESTER) | ( | MQ-1601 (Q-METER) |
| ( | CH-100 (LCR-METER) | ( | CH-852A (HIGH POT TEST METER) | ( | HL-2801 (ANALYZER) |
| ( | HK502BC (DCR-METER) | ( |  | ( |  |
| 4. MATERIALS: [ 2.0 ] [ 8 ] |
| CORE: | 02-B DR2W 6 X 8 (B:2.5 F:4.0 P:3.0) | PIN: | CP |
| WIRE: φ0.35mm 2 UEW 130℃ 0.50 kg/kpcs |
| SLEEVE: | φ6 | mm | x | 12 | mm | UL | (MARK'G: | CTC | COLOR: BLUE ) | 12 m/kpcs |
| VARNISH: ----- | BOBBIN ＆ BASE: ------ |
| COATING: | ----- | N.W: | 1.25 | kg/kpcs | PACKING: 1500PCS/BOX |
| 5.NOTE: |
| DRAWN: Yu Xinze | CHECKED:Jiang Tianming | APPROVED:Tao Guowen |